## Slide 1
EEG-Based Eye State Classification & Cognitive Monitoring

## Slide 2
INTRODUCTION
  Unlike cameras, EEG works in poor lighting, is privacy-preserving
and measures brain activity directly.
  Why it Matters: This technology is critical for monitoring driver
fatigue, improving human-computer interaction, and neurofeedback systems.

## Slide 3
PROJECT GOAL
  Analyze: Understand EEG signal patterns and data quality.
  Preprocess: Clean the data using outlier detection and scaling.
  Classify: Build and compare 6 different Machine Learning models (LR, KNN, DT, RF, SVM, MLP).
  Monitor: Calculate real-world metrics like Blink Rate, Attention Score, and Fatigue Index.

## Slide 4
TECHNICAL PIPELINE
  Load dataset (Pandas)
  Outlier removal (IQR)
  Rolling feature extraction
  StandardScaler normalization
  Train-test split (80-20)
  Model training (sklearn)
  Evaluation and Monitoring (metrics)

## Slide 5
  The system uses EEG (Electroencephalography) data to monitor brain activity in real-time:
  Input Features(x): 14 EEG Channels: AF3, F7, F3, FC5, T7, P7, O1, O2, P8, T8, FC6, F4, F8, AF4.
  Preprocessing: Data was cleaned using the Interquartile Range (IQR) method to remove noise, resulting in 10,848 clean samples.
  Feature Engineering: Rolling Window Statistics (Mean and Standard Deviation) were calculated to capture the brain's rhythm over time rather than just static points.
  Target Labels(y):
  Binary classification: 0 for "Eyes Open" and 1 for "Eyes Closed."
  Slightly imbalanced Class Distribution but acceptable for binary classification : Eyes Open: 6005 samples (55.4%), Eyes Closed: 4843 samples (44.6%)
DATASET OVERVIEW

## Slide 8
Eye-State changes are temporal events not a single-point event.
  Rolling window size = 10
  Mean, Std, Min, Max per channel
  14 original + 56 rolling = 70 features

## Slide 9
MODEL DEFINITION
The six models were chosen to represent different machine learning paradigms, allowing a comprehensive evaluation of the EEG feature space.
The goal was not just to find the best model, but to:
  Compare linear vs non-linear decision boundaries
  Compare parametric vs non-parametric methods
  Compare single models vs ensemble models
  Compare classical ML vs neural networks

## Slide 10
1. Logistic Regression
Type: Linear classifier
Why used: Baseline model
  Finds linear decision boundary
  Works well when classes are linearly separable
  Fast and interpretable
3 .Decision Tree
Type: Non-linear tree-based model
Why used: Interpretability
  Splits data using feature thresholds
  Captures non-linear relationships
  Risk of overfitting (controlled via depth)
2. K-Nearest Neighbors (KNN)
Type: Distance-based classifier
Why used: Captures local structure
  Classifies based on nearest samples
  Sensitive to scaling - StandardScaler required
  Works well with structured feature spaces
6.Multi-Layer Perceptron (MLP)
Type: Feed Forward Neural Network
Why used: Capture complex patterns
  Layer Types
  Input layer (70 features)
  Hidden layers
  Output layer (binary classification)
5. Support Vector Machine (SVM)
Type: Margin-based classifier
Why used: Handles complex boundaries
  Maximizes margin between classes
  Kernel trick enables non-linear separation
  Effective for high-dimensional data
4. Random Forest
Type: Ensemble of Decision Trees
Why used: Robust non-linear modeling
  Reduces overfitting
  Provides feature importance
  Strong performance on structured data

## Slide 11
Neural Network (MLP) Training
The MLP was the most important training process.
Optimized with Adam optimizer to handle high-dimensional EEG feature spaces efficiently.
Architecture:
  Input layer: 70 features
  Hidden layer 1: approx. 100 neurons
  Hidden layer 2: approx 50 neurons
  Output layer: 1 neuron
Activation Functions
  Hidden layers - ReLU (Avoids vanishing gradient, fast computation,sparse activation)
  Output layer- Sigmoid
Feature Scaling
  StandardScaler applied
  Zero mean
  Unit variance
Necessary for:
  KNN
  SVM
  Logistic Regression
  MLP
Train-Test Split
  80% training
  20% testing
  Stratified split (preserves label distribution)
TRAINING
The training stage was carefully designed to prevent data leakage, ensure model generalization, maintain reproducibility and enable fair model comparison.

## Slide 14
The model relies primarily on rolling statistics from occipital electrodes, which are physiologically linked to eye closure. It tells us which input variables contribute most to the model’s decision:
  Rolling (temporal) features dominate
  Occipital (O1) and Parietal (P7) regions are dominant, which aligns with known alpha activity changes during eye closure.
  Short-term extrema and variability matter more than raw amplitude.

## Slide 15
COGNITIVE MONITORING
  Cognitive metrics show the high average attention, intermittent fatigue spikes, moderate blink rate
  Blink Analysis: a fatigue indicator, blink = transition 0 - 1 - 0
Computed :blink count, rate and duration
  Attention Score: lower blink rate-higher attention
  Fatigue Index: % eye-closed samples per 1000-sample window, alert threshold: 40%

## Slide 18
CONCLUSION
  Nonlinear models outperform linear
  Rolling features are crucial
  MLP provides best generalization
  Real-time monitoring is feasible

## Slide 19
Thank You